## Slide 1: Evapotranspiration in boreal forest catchments: upscaling by process models and open GIS data
Samuli Launiainen, Aura Salmivaara, Antti-Jussi Kieloaho, Mikko Peltoniemi, and Mingfu Guan

## Slide 2: Background
Boreal mixed coniferous forests cover ~80% of land area in Finland
Forest management creates mosaic landscape
Why actual ET and its spatial variability?
  Soil moisture & biogeochemical cycles, growth and climate feedback
  Improved description of ET will reduce uncertainties in catchment models
Objectives:
Develop generic daily stand-level ET model
  validate against eddy-covariance data
Upscale to landscape scale using open data
  evaluate using annual ET from catchment water balance
”Simple, applicable at large scale, minimal calibration”

## Slide 3: Semi-distributed catchment model
INPUT 2D-GRIDS:
Conifer & deciduous LAI, tree height
Soil map, root zone organic layer depths
Catchment boundaries
Topografic wetness index TWI
DAILY FORCING
Precip, SW radiation, temperature, RH (or VPD), wind speed
DAILY GRID-OUTPUTS:
ET & components
Snow water equivalent
Organic layer & root zone moisture
Drainage from root zone
Saturation deficit ( proxy of water table)
Returnflow & dynamics of saturated area
CATCHMENT OUTLET
Streamflow
Catchment  (n x m) grid of buckets
+ TOPMODEL for streamflow
generation & returnflow
Launiainen et al. 2018, in prep.
...

## Slide 4
P
ET
Three-source Penman-Monteith
Evaporation (sublimation) of canopy intercepted rain (snow)
Canopy transpiration
Evaporation from ground
Temperature-index snow model
Two-layer bucket model
Organic layer
Root zone

## Slide 5: Leaf to canopy stomatal conductance
A net photosynthesis
g1 depends on water use strategy
gsref light-saturated stomatal conductance at D = 1 kPa & const Ca
Scots pine: gsref ~2.5 mm/s (2.2 – 2.8), b ~30 – 50 Wm-2
Birch, aspen ~4.0 – 4.5 mm/s
kp ~0.6
scale-analysis & hyperbolic light-response
gsref
Medlyn et al. 2011
’USO’
Exponential PAR within canopy
soil moisture
atm. CO2
phenology
plant traits
Leaf  canopy
Medlyn et al, 2011.
Global Change Biol. 17, 2134-2144

## Slide 6: Parameterization
Mainly from literature
Some parameters calibrated
  a single flux site, Hyytiälä, Southern Finland
1 for ground evaporation:
  multi-layer SVAT –model APES
  sub-canopy EC data
1 for transpiration
  gsref from leaf gas exchange
  check against EC data
1 for interception of rainfall:
  capacity = w x LAI, using throughfall data
APES: Launiainen et al. 2015 Ecol. Mod

## Slide 7: Site scale validation
9 EC sites from Finland & Sweden, 60 N to 68 N
LAI (1-sided) from 0.2 to 6.8 m2m-2
Pristine peatland … dense managed forests
Daily ET
  dry-canopy conditions
  Growing season (May-Oct)
Independent comparison
Model
measured

## Slide 8: Multi-source National Forest Inventory (16 X 16 m)
45 raster themes (geotiff)
Open data, 3 year update interval
> 80 0000 forest inventory plots
Landsat + DEM, topographic basemap
kNN –interpolation
LAI = M x SLA
Comparison with MODIS LAI: Härkönen et al 2015 Bor. Env. Res. 20: 181–195
1km
1,4km
http://kartta.luke.fi/index-en.html

## Slide 9: Spatial variability within catchment
Porkkavaara catchment, Eastern Finland, 64ha, 16x16m grid
ET / P
LAI –relationship non-linear; inflection point at LAI 2 to 3 m2m-2
Interception
Capacity ~ a x LAI
Snow interception
Transpiration
Saturates due to light limitations
Higher where deciduous dominant
Drought stress at coarse soils
Evaporation from ground
available energy
Gridcells with high TWI receive returnflow & behave as wet surfaces

## Slide 10: Annual evaporation ratio ET/P
21 headwater catchments over Finland. Streamflow data 1 - 10 yr / catchment
Independent comparison
Across-catchment variability primarily due to north-south gradient:
  Epot / P
  Length of snow-cover & annual snowfall
  LAI
Catchment water balance ET = P – Q
Model + parameter uncertainty

## Slide 11: Climate projections
Lompolojängänoja,
Muonio
Porkkavaara,
Sotkamo
Paunulanpuro,
Orivesi
Larger evaporative demand
Increasing ground evaporation
Higher wintertime interception
Transpiration:
  Increases in spring & early summer
  Drought-induced decrease in July-August

## Slide 12: NutSpatHy
A grid-based distributed nutrient model for predicting nitrogen (N) and phosphorous (P) leaching in forested catchments
Model key features:
  - Grid-based nutrient balance (Δstorage = release - uptake)
  - Nutrient concentration prediction (conc = storage/water_volume)
  - Export loading simulation based on SpatHy runoff prediction
  - Spatiotemporal modelling of nutrient dynamics
Mingfu Guan
FRESHHABIT (2016-2022, EU LIFE+)
Ari Lauren

## Slide 13
N and P concentration
Nutrient concentration is reasonably predicted considering the complex chemical process and a series of uncertainties of parameters and input data.
Daily and monthly N and P export loading
  Good performance in the prediction of export loading verifies the controlling role of hydrology on nutrient transport processes.
  Daily N and P export loading: NSC = 0.76, correlation coef.= 0.81
FRESHHABIT (2016-2022, EU LIFE+)
FRESHHABIT (2016-2022, EU LIFE+)

## Slide 14: Dynamic forest trafficability prediction by fusion of open data, hydrologic forecasts and harvester-measured data
Rut depth prediction
f(t, x, y)
Salmivaara, A., Launiainen, S., Ala-Ilomäki, J., Kulju, S., Laurén, A., Sirén, M., Tuominen, S., Finér, L., Uusitalo, J., Nevalainen, P., Pahikkala, T., and Heikkonen, J. 2017. Dynamic forest trafficability prediction by fusion of open data, hydrologic forecasts and harvester-measured data. Poster.
Aura Salmivaara

## Slide 15: Take home!
Daily forest ET can be predicted with simple scheme with no site / catchment-specific calibration
A three-source model seems as a good compromise
Lot of things going on:
  Forest trafficability
  Towards spatial biogeochemistry
  Radiation heterogeneity by topography & surrounding canopies
What can be done at one point should be done spatially
Codes (Python 2.7/3.x)

## Slide 16
contact: samuli.launiainen@luke.fi
Presentation available at:
https://github.com/LukeEcomod/EGU2018